## Slide 1: 3GPP 5G Technology and Self Evaluation Results
Wu Yong
3GPP Rapporteur of IMT-2020 self-evaluation
wuyong@huawei.com

## Slide 2: Table of contents
1
3GPP 5G development and submission towards IMT-2020
2
3
4
3GPP 5G technology for IMT-2020
3GPP 5G self evaluation towards IMT-2020
Conclusion

## Slide 3: ITU-R IMT-2020 vision: Extend Radio to industries
Enhance Mobile Broadband eMBB
URLLC
Ultra-Reliable and
Low Latency Communications
mMTC
Massive Machine Type Communications
IMT-2020 usage scenario
Diverse services
IMT-2020 Key capabilities
Diverse requirements
mMTC
Peak Data Rate
User Experienced
Data Rate
Spectrum Efficiency
Mobility
Latency
Connection Density
Area Traffic Capacity
Network Energy Efficiency
eMBB
URLLC
IMT-2020
Vision
Rec. ITU-R M.2083
3GPP “5G” aims to meet ITU-R’s IMT-2020 vision capabilities

## Slide 4: 3GPP 5G development timeline
Rel-16 Study phase
Q2
Q3
Q4
2019
Q2
Q3
Q4
Q1
2020
Q1
Rel-16 Study and Normative phase
Rel-16 freeze
Rel-15 freeze (incl 5G SA)
Rel-15 late drop freeze
2018
Q1
2017
Q4
Rel-15 NSA (option-3) freeze
Rel-15 NSA (option-3) ASN.1
Rel-15 ASN.1 (incl 5G SA)
Rel-15 late drop ASN.1
“Early drop”
“Main drop”
“Late drop”
Q2
Rel-16 ASN.1

## Slide 5: 3GPP 5G submission towards ITU-R
  Name : 5G
    Footnote: Developed by 3GPP as 5G, Release 15 and beyond
Submission 1: SRIT
  Component RIT: NR
  Component RIT: EUTRA/LTE
    incl. standalone LTE, NB-IoT, eMTC, and LTE-NR DC
  full 38 and 36 series, and subset of 37 series
Submission 2: NR RIT
3GPP provided complete submission templates to WP 5D#33 and acknowledgement is received.
We are Here

## Slide 6: Table of contents
1
3GPP 5G development and submission towards IMT-2020
2
3
4
3GPP 5G technology for IMT-2020
3GPP 5G self evaluation towards IMT-2020
Conclusion

## Slide 7: 3GPP 5G: NR key technical characteristics
Flexible
spectrum utilization
Flexible
frame structure
Forward compatibility
Massive MIMO
TDD
SUL
D
D
D
S
U
D
D
D
S
U
…
FDD
Minimize always-on transmissions
Keep control channel together with data channel in frequency domain
Avoid static/strict timing relations
Reserved resources

## Slide 8: 3GPP 5G: NR flexible frame structure
Flexible Frame structure
NR supports reduced guard band ratio with large component carrier bandwidth
NR Multiple SCSs enable reduced slot durations
NR PDSCH can reuse resources unused by NR PDCCH, saving large overhead especially in large bandwidth
SCS | Guard band ratio | 
15kHz | 10MHz BW: 6.4% | 40 MHz BW: 2.8%
30kHz | 20 MHz BW: 8.2% | 100 MHz BW: 1.7%
60kHz | 40 MHz BW: 8.2% | 100 MHz BW: 2.8%
SCS (kHz) | Slot duration | SCS (kHz) | Slot duration
15 | 1ms | 60 | 0.25ms
30 | 0.5ms | 120 | 0.125ms
Figure source: RWS-180007, NR Physical Layer Design: Physical layer structure, numerology and frame structure, Havish Koorapaty, Ericsson

## Slide 9: 3GPP 5G: NR Massive MIMO
Massive MIMO
NR supports up to 32 gNB ports codebook for FDD; and larger than 64 gNB ports for TDD
NR supports 12 orthogonal DM-RS ports for MU pairing, as compared to 4 orthogonal UE specific RS ports in LTE
NR overhead reduction for reference signals (RS): DMRS overhead reduction for DL/UL compared to LTE-A; no CRS.
…
…
…
…
NR Type I/II codebook
NR Type-I codebook design
NR Type-II codebook design
NR DM-RS design
Source: RWS-180008, NR Physical Layer Design: NR MIMO, Younsun Kim, Samsung

## Slide 10: 3GPP 5G: NR flexible spectrum utilization
Flexible spectrum utilization
NR supports up to 16 carrier aggregation and bandwidth part. Max BW of each carrier is 100 MHz (FR1) or 400 MHz (FR2).
NR supports FDD and semi-statically configuration of UL/DL split in TDD
NR supports operating on a TDD band with supplementary uplink (SUL) band
TDD
SUL
NR SUL band (e.g., 1.8GHz)
NR TDD band (e.g., 3.5GHz)
SUL
TDD
D
D
D
S
U
D
D
D
S
U
FR1 (450MHz – 6GHz)
FR2 (24.25GHz – 52.6GHz)
[IMT Spectrum]
[WRC-19 IMT spectrum] (24.25-27.5), (37-40.5), (40.5-42.5), (42.5-43.5), (45.5-47), (47.2-48.2), (66-71)GHz
(GHz)
20GHz
40GHz
50GHz
60GHz
70GHz
80GHz
90GHz
0.091
5
3.25
3.5
1
1
2
2.2
1.5
0.2
3.5GHz
1.4GHz
66
71
52.6
50.4
48.2
47
45.5
24.25
27.5
37
40.5
42.5
43.5
1.427
1.518
3.4
3.6
4.495
4.8
4.5GHz
30GHz
 | SCS [kHz] | Maximum aggregated bandwidth (MHz)
FR1 | 15 | 800
 | 30 | 1600
 | 60 | 1600
FR2 | 60 | 3200
 | 120 | 6400
SCS (kHz) | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 70 MHz | 80 MHz | 90 MHz | 100 MHz
 | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB
15 | 25 | 52 | 79 | 106 | 133 | 160 | 216 | 270 | N.A | N.A | N.A | N.A | N.A
30 | 11 | 24 | 38 | 51 | 65 | 78 | 106 | 133 | 162 | 189 | 217 | 245 | 273
60 | N.A | 11 | 18 | 24 | 31 | 38 | 51 | 65 | 79 | 93 | 107 | 121 | 135
Spectrum utilization for FR1
Bandwidth part
Single cell for TDD+SUL
Source: RWS-180011, NR Radio Frequency and co-existence, Xutao Zhou, Samsung
Figure source: RWS-180007, NR Physical Layer Design: Physical layer structure, numerology and frame structure, Havish Koorapaty, Ericsson
Figure source: RWS-180018, Self evaluation: Enhanced Mobile Broadband (eMBB) Evaluation results, Wu Yong, Huawei

## Slide 11: 3GPP 5G: LTE evolution
Elevation Beamforming/ Full-Dimension MIMO
Proximity services (ProSe) and vehicle-to-everything (V2X)
Shortened TTI and processing time
… …
Shortened TTI and processing time for LTE, possibility for subslot- (2 or 3 symbols long) and slot-based transmission.
A shortened processing time of n+3 (compared to n+4) for subframe-based transmissions
UE-autonomous and NW-managed resource allocation for sidelink
Distributed synchronization for no network coverage
New physical layer format for high mobility scenarios (V2X)
New cellular multicast periodicities for reduced latency
  Increased number CSI-RS ports to 12 and 16
  Beam selection
  SRS enhancements for low delay spread channels
  DMRS enhancements to increase the number of co-scheduled UEs
Source: RWS-180013, LTE evolution, Asbjörn Grövlen, Ericsson

## Slide 12: 3GPP 5G: NB-IoT and eMTC
NB-IoT
eMTC
Single-tone and 3/6/12-tone UL allocations
1-tone
3-tone
6-tone
12-tone
15 kHz
15 kHz
×12
…
3.75 kHz
×48
…
3.75 kHz
Non-anchor carriers for capacity and load-balancing
Dense subcarrier spacing
3-tone
6-tone
180 kHz
180 kHz
1.4 MHz
3- and 6-tone allocations within a PRB of a 1.4 MHz bandwidth
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
DATA
…
…
LTE subcarrier spacing
15 kHz
15 kHz
×12
…
180 kHz
LTE subcarrier spacing
PSD
f
LTE
eMTC
NB-IoT
PSD boost in bandwidth as small as 3.75 kHz
Source: RWS-180023, 3GPP’s Low-Power Wide-Area IoT Solutions: NB-IoT and eMTC, Matthew Webb, Huawei

## Slide 13: 3GPP 5G architecture
Option 3 “EN-DC”
“LTE eNB” as Master Node (MN), connected to LTE core network
“NR gNB” as Secondary Node (SN)
Option 2 NR Standalone; NR-NR DC
Option 4 “NE-DC”
“NR gNB” as MN, connected to 5G core network
“NR gNB” or “LTE eNB” as SN
Option 5 LTE to 5GC
Option 7 “NGEN-DC”
“LTE eNB” as MN, connected to 5G core network
“NR gNB” as SN
3GPP provided multiple options for smooth migration to 5G based on operator’s strategies.
Source: RWS-180009, NR Architecture, Gino Masini, Ericsson

## Slide 14: Table of contents
1
3GPP 5G development and submission towards IMT-2020
3
4
3GPP 5G self evaluation towards IMT-2020
Conclusion
2
3GPP 5G technology for IMT-2020

## Slide 15: 3GPP submission templates
According to Report ITU-R M.2411 “Requirements, Evaluation criteria, and submission templates for the development of IMT-2020”.
3GPP provided the following submission templates and preliminary self evaluation
Description templates
Characteristics templates
For SRIT (NR+LTE)
For NR RIT
Link budget template
NR in 5 test environments,
LTE in 4 test environments
Compliance templates
Based on evaluation guidelines defined in Report ITU-R M.2412.
Evaluation results for Rel-15/16
  NR RIT: 5 test environments for eMBB, URLLC and mMTC
  LTE RIT: Indoor/Dense Urban/Rural – eMBB and Urban Macro – mMTC
Self evaluation report TR37.910v16.1.0
IMT-2020 submission
Compliance templates
For SRIT (NR+LTE)
For NR RIT
On
Service, Spectrum and Technical performance requirement

## Slide 16: 3GPP Submission Templates Description templates - Characteristics
Test environment(s)
Radio interface functional aspects (multiple access, modulation, PAPR, coding scheme)
Channel tracking capabilities (e.g., pilot symbol configuration)
Physical channel structure and multiplexing
Mobility management (Handover)
Radio resource management
Frame structure
Spectrum capabilities and duplex technologies
Support of Advanced antenna capabilities
Link adaptation and power control
Power classes
Scheduler, QoS support and management, data services
Radio interface architecture and protocol stack
Cell selection
Location determination mechanisms
Priority access mechanisms
Unicast, multicast and broadcast
Privacy, authorization, encryption, authentication and legal intercept schemes
Frequency planning
Interference mitigation within radio interface
Synchronization requirements
Support for wide range of services
Global circulation of terminals
Energy efficiency
Other items
3GPP provided characteristics description for SRIT (NR+LTE) and NR RIT for all items.
The description on new and key functionalities are the basis for ITU evaluation.

## Slide 17: Characteristics Description: More references
Document | 
RWS-180004 | The 3GPP Submission
RWS-180005 | Overview of RAN aspects
RWS-180006 | System and Core Network Aspects
RWS-180007 | NR Physical Layer Design: Physical layer structure, numerology and frame structure
RWS-180008 | NR Physical Layer Design: NR MIMO
RWS-180009 | NR Architecture
RWS-180010 | NR Radio interface Protocols
RWS-180011 | NR Radio Frequency and co-existence
RWS-180023 | 3GPP’s Low-Power Wide-Area IoT Solutions: NB-IoT and eMTC
RWS-180013 | LTE evolution

## Slide 18: Self evaluation report TR 37.910
TR 37.910 v16.1.0 provides the full assessment of 3GPP 5G towards IMT-2020 requirements
 | NR | LTE
Indoor Hotspot | ✓ | ✓
Dense Urban | ✓ | ✓
Rural | ✓ | ✓
 | NR | LTE
Urban Macro | ✓ | N/A
 | NR | LTE
Urban Macro | ✓ | ✓
Future IMT
mMTC
eMBB
URLLC

## Slide 19: Peak spectral efficiency
Peak spectral efficiency:
  DL: 8 layer for FR1; 6 layer for FR2; 256QAM (NR, LTE) / 1024QAM (LTE), max code rate = 0.9258 (NR) / 0.93 (LTE)
  UL: 4 layer, 256QAM, max code rate = 0.9258 (NR) / 0.93 (LTE)
Chart: 
| LTE DSUDD (20 MHz BW, 15kHz SCS, 256QAM) | NR DDDSU (100MHz BW, 30kHz SCS, 256QAM)
UL | 17.28 | 22.8
Chart: 
| LTE DSUDD (20 MHz BW, 15kHz SCS, 256QAM) | NR DDDSU (100MHz BW, 30kHz SCS, 256QAM)
DL | 36.69 | 48.1
  NR large CC bandwidth introduces reduced guard band ratio
  NR small overhead for DL:
    For PDCCH, as low as 0.6%@100 MHz for low load; 8-layer DMRS overhead reduced to 9.5%; no CRS
  NR small overhead for UL:
    4-layer DMRS overhead reduced to 7% under UL OFDMA; “Special subframe” can be used to transmit UL data -> Overhead reduced.
  … …
Contributing technical components:
DL peak spectral efficiency (bit/s/Hz)
UL peak spectral efficiency (bit/s/Hz)

## Slide 20: Peak spectral efficiency
Various NR/LTE configurations are evaluated; see Section 5.1 of TR37.910 for details.
FR1
FR2

## Slide 21: Peak data rate
Peak data rate:
  NR Max aggregated bandwidth :
    FR1 (15 kHz SCS): 16 CC x 50 MHz/CC = 800 MHz
    FR1 (30/60 kHz SCS): 16 CC x 100 MHz/CC = 1.6 GHz
    FR2 (120 kHz SCS): 16 CC x 400 MHz/CC = 6.4 GHz
  LTE Max aggregated bandwidth:
    32 CC x 20 MHz/CC = 640 MHz
Chart: 
 | 38.6 | 171.2 | 18.9 | 64.6
For various NR configurations
Chart: 
 | 24 | 12.9
NR Peak data rate (Gbit/s)
LTE Peak data rate (Gbit/s)
For LTE FDD (256QAM) with 640 MHz BW
  Peak data rate =
    (Peak SE) x (Aggregated bandwidth)
DL
UL
DL
UL

## Slide 22: Average and 5th percentile user SE
Contributing technical components for DL:
  NR frame structure:
    NR large CC bandwidth introduces reduced guard band ratio
    NR PDCCH and PDSCH sharing allows overhead reduction, especially in large CC bandwidth
  NR Massive MIMO:
    NR Type II codebook and 12 orthogonal DMRS enhances MU-MIMO spectral efficiency especially for FDD
    NR fast CSI feedback and SRS capacity enhancement improves MU-MIMO spectral efficiency especially for TDD.
  … …
Contributing technical components for UL:
  NR large CC bandwidth introduces reduced guard band ratio
  NR DMRS overhead reduction for UL OFDMA compared to LTE-A
  NR SRS capacity enhancement accelerates UL CSI derivation
  NR OFDMA enables flexible and efficient resource allocation
  … …
2 OS for 10MHz
1 OS for 20MHz
0.5 OS for 40MHz
NR PDCCH overhead reduction for large bandwidth

## Slide 23: Average and 5th percentile user SE
Chart: 
| 32x4, DDDSU, 30kHz SCS | 64x4, DDDSU, 30kHz SCS
20 MHz BW | 13.28 | 16.1
40 MHz BW | 15.42 | 18.84
100 MHz BW | 16.89 | 20.7
Chart: 
| 32x4, DDDSU, 30kHz SCS | 64x4, DDDSU, 30kHz SCS
20 MHz BW | 0.43 | 0.49
40 MHz BW | 0.5 | 0.58
100 MHz BW | 0.54 | 0.64
NR evaluation results for Dense Urban:
  Larger CC bandwidth brings improved SE (~30%) due to guard band ratio reduction and PDCCH overhead reduction
  NR Massive MIMO: 64 TXRU brings additional gain over 32 TXRU in TDD.
NR DL average spectral efficiency (bit/s/Hz/TRxP)
NR DL 5th percentile spectral efficiency (bit/s/Hz)
Dense Urban (4 GHz)
Dense Urban (4 GHz)

## Slide 24: Average and 5th percentile user SE
Various NR configurations are evaluated. See Section 5.4 of TR37.910 for details
InH (4 GHz)
InH (30 GHz)
Dense Urban (4 GHz)
Rural (700 MHz)
NR DL average spectral efficiency (bit/s/Hz/TRxP)
NR DL 5th percentile user spectral efficiency (bit/s/Hz)

## Slide 25: Average and 5th percentile user SE
Various NR configurations are evaluated. See Section 5.4 of TR37.910 for details
InH (4 GHz)
InH (30 GHz)
Dense Urban (4 GHz)
Rural (700 MHz)
NR UL average spectral efficiency (bit/s/Hz/TRxP)
NR UL 5th percentile user spectral efficiency (bit/s/Hz)

## Slide 26: Average and 5th percentile user SE
Various LTE configurations are evaluated for Rural, Indoor and Dense Urban - eMBB. See Section 5.4 of TR37.910 for details
LTE DL average spectral efficiency, Rural (bit/s/Hz/TRxP)
LTE UL average spectral efficiency, Rural (bit/s/Hz/TRxP)
LTE DL 5th percentile user spectral efficiency, Rural (bit/s/Hz)
LTE UL 5th percentile user spectral efficiency, Rural (bit/s/Hz)
DL
UL

## Slide 27: User experienced data rate
Contributing technical components :
  For both DL and UL, carrier aggregation can be used to boost the user experienced data rate.
  For the case of where NR TDD band is in higher frequency range, TDD+SUL can benefit UL user experienced data rate :
    Usually TDD band is in higher frequency range than SUL band.
    In this case, cell edge users can be allocated to SUL band for uplink transmission where lower propagation loss is observed.
  … …
Target | Band | Required BW
DL target = 100 Mbit/s | 4 GHz (NR FDD/TDD; various antenna configuration) | 160~560 MHz BW
UL target = 50 Mbit/s | 4 GHz (NF FDD/TDD; various antenna configuration) | 120 ~ 800 MHz BW
 | 30 GHz (NR TDD, 8x32) + 4 GHz (SUL, 2x32) | 30 GHz: 1.2 GHz BW; 4 GHz: 100 MHz BW
Required bandwidth for user experienced data rate (Dense Urban)
NR fulfills user experienced data rate requirement with its supported bandwidth capability.

## Slide 28: Area traffic capacity
Area traffic capacity:
  NR Max aggregated bandwidth :
    FR1 (15 kHz SCS): 16 CC x 50 MHz/CC = 800 MHz
    FR1 (30/60 kHz SCS): 16 CC x 100 MHz/CC = 1.6 GHz
    FR2 (120 kHz SCS): 16 CC x 400 MHz/CC = 6.4 GHz
  Area traffic capacity=
    (Average SE) x (Aggregated bandwidth)
    / (Simulation area)
Frequency band | Required BW for DL target of 10 Mbit/s/m2 | 
 | 12TRxP | 36TRxP
4 GHz | 360 MHz ~ 800 MHz | 120 MHz ~ 280 MHz
30 GHz | 600 MHz ~ 1200 MHz | 200 MHz ~ 400 MHz
Required bandwidth for area traffic capacity (Indoor hotspot)
NR fulfills area traffic capacity requirement with its supported bandwidth capability.

## Slide 29: Energy efficiency
  Network energy efficiency
    Related to always-on transmissions; For NR, SSB period can be configured as long as 160ms
  Device energy efficiency
    Discontinuous reception (DRX)
    BWP adaptation for NR
    RRC_INACTIVE state for NR
Half frame
(
5
ms
)
SS block
“SSB set”
“SSB set”
periodicity
Half frame
(
5
ms
)
RMSI
SSB configuration |  | SSB set periodicity PSSB
SCS [kHz] | Number of SS/PBCH block per SSB set, L | 160ms
15kHz | 1 | 99.38%
 | 2 | 99.38%
30kHz | 1 | 99.84%
 | 4 | 99.38%
120kHz | 8 | 99.69%
 | 16 | 99.38%
240kHz | 16 | 99.69%
 | 32 | 99.38%
 | Paging cycle NPC_RF *10 (ms) | SCS (kHz) | SSB L | SSB reception time(ms) | SSB cycle (ms) | Number of SSB burst set | RRM measurement time per DRX (ms) | Transition time(ms) | Sleep ratio
RRC-Idle/Inactive | 320 | 240 | 32 | 1 | -- | 1 | 3.5 | 10 | 95.5%
 | 2560 | 15 | 2 | 1 | -- | 1 | 3 | 10 | 99.5%
 | 2560 | 15 | 2 | 1 | 160 | 2 | 3 | 10 | 93.2%
NR gNB sleep ratio under low load
NR Device sleep ratio for idle / in-active mode
NR fulfills energy efficiency requirement.

## Slide 30: Energy efficiency
  Network energy efficiency
    For LTE, FeMBMS/Unicast-mixed cell and MBMS-dedicated cell can switch off the always-on signals.
  Device energy efficiency
    Discontinuous reception (DRX)
LTE Device sleep ratio under idle mode
Cell type | Sleep ratio
FeMBMS/Unicast-mixed cell | 80%
MBMS-dedicated cell | 93.75%
LTE eNB sleep ratio under low load
 | Paging cycle NPC_RF *10 (ms) | Synchronization reception time per cycle(ms) | Synchronization cycle(ms) | Number of synchronization | RRM measurement time per DRX (ms) | Transition time (ms) | DL/UL subframe ratio | Sleep ratio
RRC-Idle | 320 | 2 | 10* | 1 | 6 | 10 | 1 | 93.1%
 | 320 | 2 | 10* | 2 | 6 | 10 | 1 | 90.0%
 | 2560 | 2 | 10* | 1 | 6 | 10 | 1 | 99.1%
 | 2560 | 2 | 10* | 2 | 6 | 10 | 1 | 98.8%
LTE fulfills energy efficiency requirement.

## Slide 31: Mobility
Chart: 
| NR FDD 1x8 SIMO, 15 kHz SCS | NR TDD 1x8 SIMO, 15 kHz SCS | NR FDD 1x8 SIMO, 15 kHz SCS | NR TDD 1x8 SIMO, 15 kHz SCS | NR FDD 1x4 SIMO, 15 kHz SCS | NR TDD 1x4 SIMO, 15 kHz SCS | NR FDD 1x4 SIMO, 30 kHz SCS | NR TDD 1x4 SIMO, 30 kHz SCS | NR FDD 1x4 SIMO, 30 kHz SCS | NR TDD 1x4 SIMO, 30 kHz SCS | NR FDD 1x4 SIMO, 60 kHz SCS | NR TDD 1x4 SIMO, 60 kHz SCS
 | 1.78 | 1.78 | 1.87 | 2.03 | 1.71 | 2.1 | 1.53 | 1.88 | 1.56 | 1.18 | 0.91 | 0.84
Mobility is evaluated using MIMO configurations.
Contributing technical components:
  NR frame structure:
    NR multiple SCSs allow to use larger sub-carrier spacing which is beneficial to combat with Doppler spread.
    NR fast CSI feedback and low processing delay helps to combat with time variation of propagation channel.
NR Mobility: Normalized traffic channel link data rate (bit/s/Hz) (Some example configurations; see Section 5.9 of TR37.910 for more details)
InH
(10km/h)
Dense Urban
(30km/h)
Rural 700 MHz
(120km/h)
Rural 700 MHz
(500km/h)
Rural 4 GHz
(120km/h)
Rural 4 GHz
(500km/h)

## Slide 32: User plane latency
Contributing technical components for NR:
  NR frame structure:
    NR larger SCSs allow slot duration reduction.
  NR Flexible configuration of DL/UL slot:
    beneficial to reduce DL or UL waiting time
  NR TDD+SUL:
    SUL provided continuous uplink transmission opportunity to reduce DL ACK feedback and UL waiting time.
    This is especially useful for synchronized network with DL dominant configurations (e.g., DDDSU).
  … …
Contributing technical components for LTE:
  Short TTI
  … …
    NR non-slot allows to use less number of OFDM symbol for data transmission, also beneficial to reduce air-interface transmission duration
    Resource mapping type B allows immediate data transmission once scheduling resource is available.

## Slide 33: User plane latency
Various configurations are evaluated for NR. See TR37.910 for more details.
NR FDD
Chart: 
| 15 kHz SCS | 30 kHz SCS | 60 kHz SCS
Mapping type A (14 OS) | 2 | 1.06 | 0.63
Mapping type A (7 OS) | 1.5 | 0.8 | 0.49
Mapping type B (7 OS) | 1.19 | 0.64 | 0.42
UP latency for NR uplink
NR TDD
NR TDD w/ SUL
NR fulfills UL user plane latency requirement for eMBB (4ms) and URLLC (1ms).
* Mapping type B (7 OS)
** Mapping type A (7 OS)
**
*
Chart: 
| 15 kHz SCS | 30 kHz SCS | 60 kHz SCS
DSUUD | 2.56 | 1.31 | 0.75
DUDU | 1.6 | 0.83 | 0.51
DDDXU | 2.57 | 1.35 | 0.75
Chart: 
| 15 kHz SCS | 30 kHz SCS
DDDSU | 3.79 | 1.96
DDDSU + SUL (15 kHz SCS) | 1.51 | 1.49
DDDSU + SUL (30 kHz SCS) | 0.82

## Slide 34: User plane latency
Chart: 
| 15 kHz | 30 kHz | 60 kHz
DSUUD | 1.9 | 0.99 | 0.58
DUDU | 1.55 | 0.81 | 0.5
DDDXU | 1.42 | 0.74 | 0.49
Various configurations are evaluated for NR. See TR37.910 for more details.
NR FDD
UP latency for NR downlink
NR TDD
* Mapping type B (7 OS)
** Mapping type A (7 OS)
NR TDD w/ SUL
Chart: 
| 15 kHz | 30 kHz | 60 kHz
Mapping type A (14 OS) | 2 | 1.04 | 0.63
Mapping type A (7 OS) | 1.25 | 0.71 | 0.44
Mapping type B (7 OS) | 1.08 | 0.59 | 0.4
Chart: 
| 15 kHz | 30 kHz
DDDSU | 1.67 | 0.9
DDDSU + SUL (15 kHz SCS) | 1.44 | 0.82
DDDSU + SUL (30 kHz SCS) | 0.82
**
*
NR fulfills DL user plane latency requirement for eMBB (4ms) and URLLC (1ms).

## Slide 35: User plane latency
Various configurations are evaluated for LTE. See TR37.910 for more details.
LTE FDD (DL)
UP latency for LTE
LTE TDD (DL)
Chart: 
| 7OS | Mixed 2OS/3OS | 3OS | 2OS
 | 2.58 | 0.88 | 1.1 | 0.73
Chart: 
| DSUDD | DSUUD
7OS | 3.1 | 3.14
7OS
7OS
Chart: 
| 7OS | Mixed 2OS/3OS | 3OS | 2OS
FDD | 2.58 | 0.88 | 1.1 | 0.73
Chart: 
| DSUUD
DSUUD | 3.73
7OS
LTE FDD (UL)
LTE TDD (UL)
LTE fulfills DL and UL user plane latency requirement for eMBB (4ms) and URLLC (1ms).

## Slide 36: Control plane latency
Contributing technical components for NR include the use of RRC_INACTIVE state, as well as other components similar to UP latency.
For LTE, the control plane latency is improved compared to Rel-10 by the use of RRC connection resume procedure, as well as by recognizing that some processing delay can be further reduced.
NR
Both FDD and TDD can reach as low as around 11ms
UE
gNB
1. Delay for RACH Scheduling Period
3. Processing delay in gNB
5. Processing delay in UE
7. Processing delay in gNB
9. Processing delay in UE
2. RACH Preamble
4. RA response
6. RRC Resume Request
8. RRC Resume
10. RRC Resume Complete
Control plane procedure
LTE
Both FDD and TDD can reach the target: 20ms
NR and LTE fulfill control plane latency requirement for eMBB and URLLC (20ms).

## Slide 37: Mobility interruption time
NR
LTE
NR fulfills 0ms mobility interruption time in the following scenarios:
Beam mobility
  When moving within the same cell, the transmit-receive beam pair of the UE may need to be changed.
  gNB can configure different beams for this UE at different slots. It ensures appropriate transmit/receive beam allocation to the UE for continuous data transmission
CA mobility
  When moving within the same PCell with CA enabled, the set of configured SCells of the UE may change.
  During these procedures, the UE can always exchange user plane packets with the gNB during transitions, because the data transmission between the UE and the PCell is kept.
LTE fulfills 0ms mobility interruption time in the following scenarios:
PCell mobility
  See details in Section 5.10 in TR37.910
DC mobility
  See details in Section 5.10 in TR37.910.
NR and LTE fulfill mobility interruption time requirement for eMBB and URLLC (0ms).

## Slide 38: Reliability
Contributing technical components:
  NR frame structure with multiple SCSs is beneficial to reduce the delay.
  Slot aggregation and lower MCS is beneficial to ensure the reliability.
Chart: 
| 2x2 SU-MIMO,14os slot, Slot aggregation, (1 PDCCH+2 PDSCH) | 2x2 SU-MIMO,4os non-slot, HARQ re-tx (2 PDCCH+2 PDSCH) | 2x2 SU-MIMO, 4os non-slot, One shot (1 PDCCH+1 PDSCH) | 2x2 SU-MIMO, 14os slot, One shot (1 PDCCH+1 PDSCH) | 2x2 SU-MIMO 7os non-slot, One-shot (1 PDCCH+1 PDSCH) | 2x2 SU-MIMO, 4os non-slot, Slot aggregation (1 PDCCH+2 PDSCH)
 | 1 | 1 | 1 | 1 | 0.99999 | 1
NR DL reliability
4 GHz
700 MHz
Chart: 
| 2x2 SU-MIMO, 4os non-slot Grant free, One shot (1 PUSCH) | 1x16 SIMO, 14os slot, Grant free, One shot (1 PUSCH) | 1x8 SIMO, 14os, Grant free, 2 repetitions (2 PUSCH) | 2x2 SU-MIMO, 4os non-slot, Grant free, 2 repetitions (2 PUSCH) | 1x8 SIMO, 14os slot, Grant free One shot (1 PUSCH) | 1x8 SIMO, 7os non-slot, One shot (1 PUSCH)
 | 0.99999 | 1 | 1 | 1 | 1 | 0.99999
NR UL reliability
NR fulfills reliability requirement.

## Slide 39: Connection density
Connection density for NR, NB-IoT and eMTC are evaluated. See TR37.910 for more details.
ISD (meter) | Required bandwidth (kHz) | Connection density (device/km2) | Target (device/km2)
500 | 180 | 36,000,000 | 1,000,000
1732 | 180 | 1,503,000 | 
NR fulfills connection density requirement
NR connection density (1x2 SIMO, 15kHz SCS)
NB-IoT and eMTC fulfills connection density requirement
LTE connection density
Full buffer system level simulation followed by link level simulation; packet arrival rate: 1 packet / 2 hour / device;
Chart: 
| 1x2 SIMO (Required bandwidth = 180 kHz)
NB-IoT | 43.6918
eMTC | 35.2355
Chart: 
| 1x2 SIMO (Required bandwidth = 180 kHz)
NB-IoT | 2.3353
eMTC | 1.2129
ISD=500 m
ISD=1732 m
Connection density (million)
(Channel model B)
(Channel model A)

## Slide 40: Link budget
Chart: 
| PDCCH | PDSCH | PUCCH | PUSCH
Indoor Hotspot (4GHz, TDD) | 401.36 | 233.2 | 892.14 | 223.37
Chart: 
| PDCCH | PDSCH | PUCCH | PUSCH
Dense Urban (4GHz, TDD) | 600.38 | 476.58 | 283.67 | 158.64
Chart: 
| PDCCH | PDSCH | PUCCH | PUSCH
Rural (700MHz, FDD) | 5467.81 | 4039.44 | 2816.14 | 1540.15
Chart: 
| PDCCH | PDSCH | PUCCH | PUSCH
Urban Macro-URLLC (700MHz, FDD) | 848.33 | 1004.6 | 303.17 | 316.01
Link budget
Link budget are provided for NR. See link budget templates for details
Indoor Hotspot (4GHz, TDD)
Dense Urban (4GHz, TDD)
Rural (700MHz, FDD)
Urban Macro-URLLC (700MHz, FDD)
NR link budget for some configurations

## Slide 41
Link budget
Link budget are provided for LTE. See link budget templates for details
Rural (700MHz, FDD)
Urban Macro-eMTC (700MHz, FDD)
Chart: 
| PDCCH | PDSCH | PUCCH | PUSCH
Rural (700MHz, FDD) | 4591.78 | 3352.06 | 2613.96 | 1387.6
Chart: 
| PDCCH | PDSCH | PUCCH | PUSCH
Urban Macro-mMTC (eMTC) | 1588.54 | 1694.91 | 1680.52 | 1547.45
Chart: 
| NPDCCH | NPDSCH | NPUSCH (Format 2) | NPUSCH (Format 1)
Urban Macro-mMTC (NB-IoT) | 1778.97 | 1886.93 | 1760.78 | 1824.14
Urban Macro-NB-IoT (700MHz, FDD)
LTE link budget for some configurations

## Slide 42: Table of contents
1
3GPP 5G development and submission towards IMT-2020
4
Conclusion
2
3GPP 5G technology for IMT-2020
3
3GPP 5G self evaluation towards IMT-2020

## Slide 43: 3GPP Compliance to Service and Spectrum Requirement
 | Service capability requirements | SRIT (NR+LTE) | NR RIT
5.2.4.1.1 | Support for wide range of services Is the proposal able to support a range of services across different usage scenarios (eMBB, URLLC, and mMTC)?: YES/NO Specify which usage scenarios (eMBB, URLLC, and mMTC) the candidate RIT or candidate SRIT can support. | YES The SRIT can support eMBB, URLLC and mMTC usage scenarios. | YES The NR RIT can support eMBB, URLLC and mMTC usage scenarios.
 | Spectrum capability requirements | SRIT (NR+LTE) | NR RIT
5.2.4.2.1 | Frequency bands identified for IMT Is the proposal able to utilize at least one frequency band identified for IMT in the ITU Radio Regulations?:  YES /NO Specify in which band(s) the candidate RIT or candidate SRIT can be deployed. | YES LTE RIT supports the IMT band from 450 MHz to 5925 MHz. NR RIT supports the IMT band from 663 MHz to 5000 MHz. See Section 5.2.3.2.8.3 in characteristics template for details. | YES NR RIT supports the IMT band from 663 MHz to 5000 MHz, including 3.3-3.8; 3.3-4.2 GHz. See Section 5.2.3.2.8.3 in characteristics template for NR RIT for details.
5.2.4.2.2 | Higher Frequency range/band(s) Is the proposal able to utilize the higher frequency range/band(s) above 24.25 GHz?: YES Specify in which band(s) the candidate RIT or candidate SRIT can be deployed. (NOTE 1) | YES NR RIT supports 24.25-27.5; 27.5-28.35; 26.5-29.5; 37-40 GHz. | YES NR RIT supports 24.25-27.5; 27.5-28.35; 26.5-29.5; 37-40 GHz.
NOTE 1 – In the case of the candidate SRIT, at least one of the component RITs need to fulfil this requirement.

## Slide 44: 3GPP Compliance to Technical Performance Requirement
Chart: 
 | 16.88 | 19.91 | 22.33 | 17.37 | 21.11 | 19.29 | 15.2 | 11.4 | 22.48 | 15.6 | 21.3 | 10.6
Chart: 
 | 0.59 | 1.18 | 0.81 | 0.57 | 2.11 | 0.63 | 0.43 | 0.6 | 0.63 | 0.34
Chart: 
 | 3.85 | 4.76 | 4.58 | 3.22 | 2.91 | 2.73 | 2.75 | 2.09
Chart: 
 | 1530000
Chart: 
 | 16.8 | 22.8
Chart: 
 | 144 | 73
Chart: 
 | 48.9 | 25.8
Chart: 
 | 140.2 | 64.6
Peak data rate (Gbit/s)
Peak spectral efficiency (bit/s/Hz)
DL
UL
DL
UL
User experienced data rate (Mbit/s)
Area traffic capacity (Mbit/s/m2)
DL
UL
DL
UL
5th percentile user spectral efficiency (bit/s/Hz)
DL
UL
Average spectral efficiency (bit/s/Hz/TRxP)
Chart: 
 | 0.28 | 0.28 | 0.23 | 0.24
Chart: 
 | 11.3 | 11.3
Chart: 
 | 1530000
Chart: 
 | 0.01 | 0.01
Chart: 
 | 0.01 | 0.01
User plane latency (ms)
Control plane latency (ms)
Mobility interruption time (ms)
Reliability (within 1ms)
0
0
>99.99999%
1,503,000
Connection density (#/km2)
DL
UL
DL
UL
eMBB
eMBB
URLLC
URLLC
eMBB
URLLC
eMBB
URLLC
DL
UL
ISD=1732m
InH
Dense Urban
Rural
Rural (LMLC)
Indoor Hotspot
Dense Urban
Rural (120km/h; 500km/h)
Mobility (bit/s/Hz)
Energy efficiency
High sleep ratio and long sleep duration
Chart: 
 | 1530000
Bandwidth (GHz)
Up to 6.4GHz
700MHz
4GHz
InH
Dense Urban
Rural
Rural (LMLC)
~6x IMT-Advanced
NR fulfills all the technical requirements.
>1.5x IMT-2020 Req.
<<1ms
Pe<1x10-6
NR
DL
UL

## Slide 45: 3GPP Compliance to Technical Performance Requirement
Chart: 
 | 1530000
Chart: 
 | 0.42 | 0.52 | 0.29 | 0.46 | 0.54 | 0.41 | 0.22 | 0.07
Chart: 
 | 11.88 | 14.91 | 11.22 | 14.75 | 6.86 | 8.84 | 7.68 | 4.3 | 10.5 | 3.36
Chart: 
 | 2.6 | 1.99 | 2.79 | 2.59
Chart: 
 | 0.73 | 0.73 | 0.63 | 0.63
Chart: 
 | 10.2 | 10.2
Chart: 
 | 105.43 | 65.12
Chart: 
 | 47.1 | 20.3
Chart: 
 | 30.1 | 12.9
Chart: 
 | 1530000
Peak data rate (Gbit/s)
Peak spectral efficiency (bit/s/Hz)
DL
UL
DL
UL
User experienced data rate (Mbit/s)
Area traffic capacity (Mbit/s/m2)
5th percentile user spectral efficiency (bit/s/Hz)
DL
UL
Average spectral efficiency (bit/s/Hz/TRxP)
DL
UL
Chart: 
 | 11.3 | 11.3
Chart: 
 | 0.01 | 0.01
Chart: 
User plane latency (ms)
Control plane latency (ms)
Mobility interruption time (ms)
Reliability (within 1ms)
0
0
2,335,000
Connection density (#/km2)
DL
UL
DL
UL
eMBB
eMBB
URLLC
URLLC
eMBB
URLLC
eMBB
URLLC
ISD=1732m
Rural
Energy efficiency
High sleep ratio and long sleep duration
Chart: 
 | 1530000
Bandwidth (GHz)
Up to 640MHz
Not evaluated in TR37.910
20
20
Rural (120km/h; 500km/h)
700 MHz
Mobility (bit/s/Hz)
0.73
LTE fulfills the technical performance requirements for required number of test environments.
LTE
Indoor Hotspot
Dense Urban
InH
Dense Urban
Rural
(LMLC)
Rural
(LMLC)
Rural
InH
Dense Urban

## Slide 46: Conclusion
Usage scenario | Sub-items | Evaluation method | Test environment |  |  |  | 
 |  |  | eMBB |  |  | mMTC | URLLC
 |  |  | Indoor hotspot | Dense urban | Rural | Urban macro | Urban macro
eMBB | Peak data rate | Analysis | ✓ | ✓ | ✓ |  | 
 | Peak spectral efficiency | Analysis | ✓ | ✓ | ✓ |  | 
 | User experienced data rate | Analysis, or SLS (for multi-layer) |  | ✓ |  |  | 
 | 5th percentile user spectral efficiency | SLS | ✓ | ✓ | ✓ |  | 
 | Average spectral efficiency | SLS | ✓ | ✓ | ✓ |  | 
 | Area traffic capacity | Analysis | ✓ |  |  |  | 
 | Energy efficiency | Inspection | ✓ | ✓ | ✓ |  | 
 | Mobility | SLS + LLS | ✓ | ✓ | ✓ |  | 
eMBB, URLLC | User plane latency | Analysis | ✓ | ✓ | ✓ |  | ✓
 | Control plane latency | Analysis | ✓ | ✓ | ✓ |  | ✓
 | Mobility interruption time | Analysis | ✓ | ✓ | ✓ |  | ✓
URLLC | Reliability | SLS + LLS |  |  |  |  | ✓
mMTC | Connection density | SLS + LLS, or Full SLS |  |  |  | ✓ | 
General | Bandwidth and Scalability | Inspection | ✓ | ✓ | ✓ | ✓ | ✓
Both 5G SRIT and NR RIT are compliant with all IMT-2020 requirements

## Slide 47: Acknowledgement

## Slide 48: Thank you!